## Slide 1: Modeling the Formation of Secondary Organic Aerosol (SOA) in 0-D Box model framework
Special topic presentation
Samiha Binte Shahid
May 5, 2023

## Slide 2: Outline
Motivation
Creating a Secondary Organic Aerosol (SOA) Model in 0-D box model framework
Parameters of SOA model
Verification of the SOA model
Future work and SOA model set-up

## Slide 3
Motivation
SAPRC box model doesn’t have aerosol model.
Framework of 0-D Atmospheric modeling (F0AM) doesn’t have a thermodynamic equilibrium gas-particle partitioning model.
In the Thornton et al.2018 paper, “A Near-Explicit Mechanism Evaluation of Isoprene Photochemical Secondary Organic Aerosol Formation and Evolution: Simulation of Multiple Chamber Experiments with and without Added NOx” they developed a kinetic SOA model that is incorporated with F0AM box model. This is more suitable for explicit mechanisms such as- The Master Chemical Mechanism (MCM), Generator for Explicit Chemistry and Kinetics of Organics in the Atmosphere (GECKO).
My future research work needs a thermodynamic equilibrium partitioning SOA model to use with condensed mechanism- SAPRC-07, SAPRC-18.

## Slide 4
Integration SOLVER
Species_0 + OH  Species_1 , k1
Species_1 + OH  Species_2, k2
Species_2 + OH  Species_3, k3
Species_3 + OH  Species_4, k4
Species_3 + condensation  Species_3p, k3_condense
Species_3p + evaporation  Species_3, k3_evaporation
Species_4 + condensation  Species_4p, k4_condense
Species_4p + evaporation  Species_4, k4_evaporation
Species_3p + OH 
Species_4p + OH 
Particle-phase reaction file
Gas-particle partitioning reaction file
Gas-phase reaction file
Kinetic SOA model

## Slide 5
Creating a Secondary Organic Aerosol (SOA) Model in 0-D box model framework
Thermodynamic equilibrium SOA model.
Incorporated the CMAQ-AERO-07 SOA scheme and parameters.
The concentration of reaction products resulting from VOC oxidation in the gas phase mechanism is time-dependent, and this information is fed into the Secondary Organic Aerosol (SOA) model. The SOA model then calculates the gas-particle partitioning of the reaction products and updates the gas-phase concentration accordingly. This updated information is then passed back to the gas-phase integration solver for further processing.
The SOA model has been written in a way allows for easy updates to the SOA parameters. This ensures that the model can be adapted to new scheme and parameters.

## Slide 6
The F0AM-CMAQ Aerosol model Scheme

## Slide 7
The F0AM-CMAQ Aerosol model Scheme: Linking Gas-Phase mechanism to SOA model
Reaction encounters are added to volatile organic compound (VOC) oxidation reaction which is passed on to the SOA model-
The concentration of product is directly passed on to the SOA model-

## Slide 8
The F0AM-CMAQ Aerosol model Scheme: SOA partitioning model parameters
The parameters in SOA-partitioning model requires- alpha, cstar, enthalpy, molecular weight of the model species.

## Slide 9
SVLIM1, SVLIM2..
TRPRXN
APINRXN
N
SOA-Partitioning Model

## Slide 10
SOA-Partitioning Model

## Slide 11
X
Y
upb
lwb
N1 = (lwb + upb)/2
if f(N1) +ve:
N2 = (N1 + upb) /2
If f(N1) –ve:
N2 = (N1 + lwb) /2
N1
F(N1)
SOA-Partitioning Model

## Slide 12
SOA Model verification

## Slide 13
SOA Model verification

## Slide 14
SOA Model verification

## Slide 15
The VBS in SOA model. The enthalpy value is assumed.
SOA Model verification

## Slide 16
Output from SOA model
SOA Model verification

## Slide 17
Output from SOA model
SOA Model verification

## Slide 18
Output from SOA model: Temperature sensitivity test
T= 298 K
T= 310 K
SOA Model verification

## Slide 19
SOA Model verification

## Slide 20
input in SOA model
LIM + OH  0.24*SVLIM1 + 0.16*SVLIM2 + 0.04*SVLIM3 (gas-phase reaction)
The gas-phase module integrates following differential equations-
Input of gas-phase module:
Initial concentration: [2.5e11, 0, 0, 0]
This gets updated from aerosol module.
Rate of reaction K : 3.4e-4 s-1
time-step (dt) = 0.3s
Total time = 60s
Output of gas-phase module:
Time dependent concentration of SVLIM1, SVLIM2, SVLIM3.
Gas-phase module
SVLIM1  ALIM1
SVLIM2  ALIM2
SVLIM3  ALIM3
Initial concentration:
Output from gas-phase module SVLIM1, SVLIM2, SVLIM3
Initial aerosol concentration: 1e-23 ug/m3
Parameter dataset:
og_mw is molecular weight of gas-phase species (SVLIM1, SVLIm2, SVLIM3)
op_mw is molecular weight of aerosol-phase species (ALIM1, ALIM2, ALIM3)
Meteorology:
T=298 K
P = 101325 pa
Output:
Concentration of ALIM1, ALIM2, ALIM3 in ug/m3
Updates SVLIM1, SVILIM2 and SVLIM3 concentration which is passed on to gas-phase module.
Aerosol module
SOA Model verification

## Slide 21
Output from SOA model
Output form the gas-phase reaction solver. This figures show as limonene decays the products are forming. This figure doesn’t show the updated concentration of the gas-phase products from the aerosol module.
SOA Model verification

## Slide 22
Output from SOA model
SOA Model verification

## Slide 23
Output from SOA model
SOA Model verification

## Slide 24: Thank you